## Slide 1
QUESTION 1
Preparing a
Greenhouse Gas Inventory
What to count, where to draw the line, and what the answer changes.
Worked on a 120,000 barrel-per-day Nigerian refinery
GROUP C (29 MEMBERS)
Notes: Open on the legal duty, not the theory: Climate Change Act 2021 section 24 makes an annual emissions report compulsory for any entity with 50 or more employees. This is a filing, not a gesture.

## Slide 2
THE FIRST DECISION
Three scopes. One fence.
The scopes exist so that two companies never count the same tonne twice.
SCOPE 1
Direct
Everything burned, flared,
vented or leaked inside
your fence.
SCOPE 2
Indirect — energy
The power station that
runs your lights.
SCOPE 3
Indirect — everything else
Your crude supplier, and
every vehicle burning the
diesel you sold.
Scope 1 and 2 are what you control. Scope 3 is what you cause.
Preparing a GHG inventory for a typical refinery
2
Notes: Analogy, used once: Scope 1 is the smoke from your own chimney. Scope 2 is the smoke from the power station that runs your lights. Scope 3 is everyone else's chimney that exists because of you. Do not use a second analogy later — it reads as condescension.

## Slide 3
SCOPE 1 — 1.60 MILLION TONNES
Two sources carry four fifths of it.
A refinery is not one chimney. It is about a dozen distinct mechanisms.
Fired heaters, boilers and CHP
60%
0.96 Mt
FCC catalyst regeneration
20%
0.32 Mt
Hydrogen plant (SMR)
9%
0.14 Mt
Flaring
4%
0.064 Mt
Fugitives and venting
3%
0.048 Mt
Sulphur, coker, water, mobile
4%
0.064 Mt
The two most often missed: the FCC burns no purchased fuel, and the hydrogen plant releases CO₂ from the reaction, not the flame.
Preparing a GHG inventory for a typical refinery
3
Notes: FCC = Fluid Catalytic Cracking; its regenerator burns coke off the catalyst, so it has no fuel meter and teams that count fuel meters miss a fifth of the site. SMR = Steam Methane Reforming. Both acronyms are defined on the slide the first time they appear.

## Slide 4
THE NUMBER THAT CHANGES THE CONVERSATION
87% of the footprint leaves
the gate in a tanker.
8.3%
87.0%
Scope 1
1.60 Mt
Scope 2
0.08 Mt
Scope 3 — customers burning our fuel
16.7 Mt
Scope 3 — all other
0.80 Mt
19.2 Mt
total CO₂e
across all scopes
Every efficiency lever works on the 8.8%. Moving the 87% is a question about what we sell.
Preparing a GHG inventory for a typical refinery
4
Notes: This is the slide the room will remember. Give it time and say the last line slowly. Scope 1 + 2 = 1.68 Mt = 8.8% of 19.2 Mt. Category 11 alone = 16.7 Mt = 87%. Reporting Scope 1 and 2 alone and calling it a footprint is the standard criticism of refiners.

## Slide 5
FROM INVENTORY TO DECISION
Measure it well, then act on it.
An inventory that changes no decision was a bookkeeping exercise.
HOW WE MEASURE
1
Continuous monitoring in the stack
2
Mass balance — carbon in, carbon out
3
Engineering calculation
4
Published emission factor
Best evidence at the top. Say which you used.
WHAT WE DO ABOUT IT
Energy and heat integration
3–8%
Methane leak detection
1–3%
Flare gas recovery
2–4%
Capture on the hydrogen plant
7–9%
Cut to Scope 1, cheapest first.
An inventory is a strategy document that happens to be written in tonnes.
Notes: Close on the decision, not a summary. Do not re-list the scopes. If asked about cost ranking: the standard tool is a marginal abatement cost curve; the alternatives are a simple payback ranking or an internal carbon price applied to every investment case.